Lessons: 00.Arduino-examples
01. Basics
Version: 0.0.4, Date: 2016-10-22

---
Contents
- Bare Minimum
- Blink
  - Assignment
  - On Off
  - Set Clear
  - Toggle
  - RTT Delay
  - Watchdog Delay
- Digital Read Serial
- Fade
- Analog Read Serial
- Voltage Read Serial

---
Bare Minimum

---
Bare Minimum Notes
- Intentionally left blank?
- Something must be missing?
- Cosa has default setup() and loop() functions.
- The sketch can skip one (or both).

---
Blink
#include “Cosa/OutputPin.hh” // Explicit include header file
OutputPin led(Board::LED); // Output Pin Instance for LED
void loop()
{
  led.write(1); // Turn LED on and off
  delay(1000); // With one second delay
  led.write(0);
  delay(1000);
}

---
Blink Notes
- Explicit include of components used in the sketch.
- Pins are symbols e.g. Board::LED.
- The setup() not needed.
- Pin initiated by the constructor.
- The OutputPin class allows several methods of setting the pin:
  - Pin.write(value)
  - Pin = value
  - Pin.on(), Pin.off()
  - Pin.set(), Pin.clear()
  - Pin.toggle()

---
Blink Assignment
#include “Cosa/OutputPin.hh”
OutputPin led(Board::LED); // Output Pin Instance for LED
  led = 1; // Turn LED on and off
  delay(1000); // With one second delay
  led = 0;
  delay(1000);

---
Blink On Off
#include “Cosa/OutputPin.hh” // Explicit include header file
OutputPin led(Board::LED); // Output Pin Instance for LED
  led.on(); // Turn LED on and off
  delay(1000); // With one second delay
  led.off();
  delay(1000);

---
Blink Set Clear
#include “Cosa/OutputPin.hh” // Explicit include header file
OutputPin led(Board::LED); // Output Pin Instance for LED
  led.set(); // Turn LED on and off
  delay(1000); // With one second delay
  led.clear();
  delay(1000);

---
Blink Toggle
#include “Cosa/OutputPin.hh” // Explicit include header file
OutputPin led(Board::LED); // Output Pin Instance for LED
  led.toggle(); // Change LED state
  delay(1000); // Every second

---
Alternative delay()
- The default delay() is implemented with busy-wait. More efficient is to use the Real-Time Timer (RTT) or the Watchdog.
- The RTT gives a hardware timer based clock with one milli-second tick. It also implements micros() and millis(), and allows low-power mode (Timer2).
- The Watchdog gives additional low-power but with less accurate and with a highest resolution of 16 ms per tick.

---
Blink RTT Delay
#include “Cosa/OutputPin.hh” // Explicit include header files
#include “Cosa/RTT.hh”
OutputPin led(Board::LED); // Output Pin Instance for LED
void setup()
  RTT::begin(); // Start Real-Time Timer
  led.on(); // Turn LED on
  delay(1000); // Delay 1000 ms
  led.off(); // Turn LED off
  delay(1000); // Delay 1000 ms

---
Blink Watchdog Delay
#include “Cosa/OutputPin.hh” // Explicit include header files
#include “Cosa/Watchdog.hh”
OutputPin led(Board::LED); // Output Pin Instance for LED
void setup()
  Watchdog::begin(); // Start Watchdog
  led.on(); // Turn LED on
  delay(1000); // Delay 1000 ms
  led.off(); // Turn LED off
  delay(1000); // Delay 1000 ms

---
Digital Read Serial
#include “Cosa/InputPin.hh” // Explicit include header files
#include “Cosa/IOStream.hh”
#include “Cosa/UART.hh”
InputPin button(Board::D2); // Input Pin Instance for D2
IOStream ios(&uart); // IOStream Instance bound to UART
void setup()
  uart.begin(9600); // Start UART and use 9600 baud
  ios << button << endl; // Print digital pin reading
  delay(100); // every 100 ms

---
Digital Read Serial Notes
- Component initialization in setup() i.e. the uart is initiated to 9600 baudrate and default format (8-N-2).
- IOStream instance ios delegates to UART which implements the IOStream::Device interface.
- IOStream print with operator<< and endl.
- The Pin value is read when the identifier is used in an expression (value-of-pin).

---
Fade
#include "Cosa/PWMPin.hh" // Explicit include header file
PWMPin led(Board::PWM3); // PWM Pin Instance on PWM3/D9
int brightness = 0; // Current brightness level
int fadeAmount = 5; // Brightness adjust amount
void setup()
  led.begin(); // Start the PWM pin
  led = brightness;
  brightness += fadeAmount;
  if (brightness <= 0 || brightness >= 255)
    fadeAmount = -fadeAmount;
  delay(10);

---
Analog Read Serial
#include “Cosa/AnalogPin.hh” // Explicit include header files
#include “Cosa/IOStream.hh”
#include “Cosa/UART.hh”
AnalogPin sensor(Board::A0); // Analog Pin Instance for A0
IOStream ios(&uart); // IOStream Instance bound to UART
void setup()
  uart.begin(9600); // Start UART and use 9600 baud
  AnalogPin::powerup(); // Start ADC module
  ios << sensor << endl; // Print analog pin reading
  delay(100); // Every 100 ms

---
Analog Read Serial Notes
- The ADC hardware module is not automatically started by Cosa.
- A sketch that used AnalogPin needs to powerup ADC.

---
Voltage Read Serial
#include “Cosa/AnalogPin.hh” // Explicit include header files
#include “Cosa/IOStream.hh”
#include “Cosa/UART.hh”
AnalogPin sensor(Board::A0); // Analog Pin Instance for A0
IOStream ios(&uart); // IOStream Instance bound to UART
void setup()
  uart.begin(9600); // Start UART and use 9600 baud
  AnalogPin::powerup(); // Start ADC module
void loop() // Convert to voltage and print
  float voltage = sensor * (5.0 / 1023.0);
  ios << voltage << endl;
  delay(100);

---
License: LGPL-2.1
Copyright (C) 2016, Mikael Patel
This library is free software; you can redistribute it and/or modify it under the terms of the GNU Lesser General Public License as published by the Free Software Foundation; either version 2.1 of the License, or (at your option) any later version.
This library is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU Lesser General Public License for more details.