Lessons: 00.Arduino-examples
01. Basics
Version: 0.0.3, Date: 2016-10-21

---
Contents
- AnalogReadSerial
- BareMinimum
- Blink
- BlinkToggle
- BlinkRTTDelay
- BlinkWatchdogDelay
- DigitalReadSerial
- Fade
- VoltageReadSerial

---
AnalogReadSerial
#include “Cosa/AnalogPin.hh” // Explicit include header files
#include “Cosa/IOStream.hh”
#include “Cosa/UART.hh”
AnalogPin sensor(Board::A0); // Analog Pin Instance for A0
IOStream ios(&uart); // IOStream Instance connected UART
void setup()
{
  uart.begin(9600); // Start UART and use 9600 baud
  AnalogPin::powerup(); // Start ADC module
}
void loop()
  ios << sensor << endl; // Print analog pin reading
  delay(100); // Delay 100 ms

---
AnalogReadSerial Notes
- Explicit include of components used in the sketch.
- Pins are symbols e.g. Board::A0.
- Component initialization in setup().
- IOStream print with operator << and endl.
- Default busy-wait delay().
- Including and initiating the Watchdog will allow low-power sleep mode during delay().

---
BareMinimum

---
BareMinimum Notes
- Something missing?
- Cosa has a default setup() and loop() function. The sketch can skip one or both.

---
Blink
#include “Cosa/OutputPin.hh”
OutputPin led(Board::LED); // Output Pin Instance for LED
  led.on(); // Turn LED on and off
  delay(1000); // With one second delay
  led.off();
  delay(1000);

---
Blink Notes
- This sketch does not need a setup().
- Pin initialization is done by the constructor.
- The OutputPin class allow several methods of accessing:
  - Pin.on(), Pin.off()
  - Pin.set(), Pin.clear()
  - Pin.toggle()
  - Pin = value

---
BlinkRTTDelay
#include “Cosa/OutputPin.hh”
#include “Cosa/RTT.hh”
OutputPin led(Board::LED); // Output Pin Instance for LED
void setup()
  RTT::begin(); // Start Real-Time Timer
  led.on(); // Turn LED on
  delay(1000); // Delay 1000 ms
  led.off(); // Turn LED off
  delay(1000); // Delay 1000 ms

---
BlinkToggle
#include “Cosa/OutputPin.hh”
OutputPin led(Board::LED); // Output Pin Instance for LED
  led.toggle(); // Change LED state
  delay(1000); // Every second

---
BlinkWatchdogDelay
#include “Cosa/OutputPin.hh”
#include “Cosa/Watchdog.hh”
OutputPin led(Board::LED); // Output Pin Instance for LED
void setup()
  Watchdog::begin(); // Start Watchdog
  led.on(); // Turn LED on
  delay(1000); // Delay 1000 ms
  led.off(); // Turn LED off
  delay(1000); // Delay 1000 ms

---
DigitalReadSerial
#include “Cosa/InputPin.hh” // Explicit include header files
#include “Cosa/IOStream.hh”
#include “Cosa/UART.hh”
InputPin button(Board::D2); // Input Pin Instance for D2
IOStream ios(&uart); // IOStream Instance connected UART
void setup()
  uart.begin(9600); // Start UART and use 9600 baud
  ios << button << endl; // Print digital pin reading
  delay(100); // Delay 100 ms

---
Fade
#include "Cosa/PWMPin.hh" // Explicit include header files
PWMPin led(Board::PWM3); // PWM Pin Instance on PWM3/D9
int brightness = 0; // Current brightness level
int fadeAmount = 5; // Brightness adjust amount
void setup()
  led.begin();
  led = brightness;
  brightness += fadeAmount;
  if (brightness <= 0 || brightness >= 255)
    fadeAmount = -fadeAmount;
  delay(10);

---
VoltageReadSerial
#include “Cosa/AnalogPin.hh” // Explicit include header files
#include “Cosa/IOStream.hh”
#include “Cosa/UART.hh”
AnalogPin sensor(Board::A0); // Analog Pin Instance for A0
IOStream ios(&uart); // IOStream Instance connected UART
void setup()
  uart.begin(9600); // Start UART and use 9600 baud
  AnalogPin::powerup(); // Start ADC module
  float voltage = sensor * (5.0 / 1023.0);
  ios << voltage << endl;
  delay(100);